## Slide 1
Istanbul, 10-11 November 2011.
Joint Research Centre, European Commission, Ispra, Italy
AOP Measurements
and
NN Bio-Optical Algorithms
for the Western Black Sea
Giuseppe Zibordi, Jean-Francois Berthon,
Davide D’Alimonte and Elisabetta Canuti

## Slide 2
In-Water Radiometry
G.Zibordi, F. Mélin, S. B. Hooker, D. D’Alimonte and B. Holben. IEEE Transactions in Geoscience and Remote Sensing , 42:401-415, 2004 .
~0.543
Fundamentals
Courtesy of S. Mc Lean
Satlantic Inc., Halifax
Extrapolation interval
z1
z2

## Slide 3
In-Water Radiometry: Products
Water leaving radiance
[mW cm-2 mm-1 sr-1]
Normalized LW
[mW cm-2 mm-1 sr-1]
Remote sensing reflectance
[sr-1]
Q-factor at nadir
[sr]
Irradiance reflectance
[-]
Diffuse attenuation coefficient
[m-1]

## Slide 4
LWN Uncertainties (in-water)
Source | LWN |  |  |  | 
 | 412 | 443 | 488 | 551 | 667
Absolute calibration | 2.8 | 2.8 | 2.8 | 2.8 | 2.8
Sensitivity change | 0.3 | 0.3 | 0.3 | 0.3 | 0.3
Correction | 2.2 | 1.7 | 1.1 | 0.6 | 2.6
Cf/Q | 0.3 | 0.4 | 0.8 | 0.9 | 0.5
Ed(0+) | 1.6 | 1.6 | 1.6 | 1.6 | 1.6
E0 | 0.5 | 1.9 | 0.8 | 0.1 | 0.2
Environmental effects | 1.5 | 1.1 | 1.2 | 1.3 | 2.8
Quadrature sum | 4.2 | 4.3 | 3.8 | 3.7 | 5.0
Notes: 5

## Slide 5
BiOMaP measurement stations (2000-2004)
G. Zibordi, J.-F. Berthon, F. Mélin and D. D’Alimonte. Cross-site consistent in situ measurements for satellite ocean color applications: the BiOMaP radiometric dataset. Remote Sensing of Environment,115, 2104–2115, 2011.
BiOMaP measurements are produced applying cross-site identical and consolidated: technology, measurement and calibration protocols, processing codes and quality assurance criteria.
BiOMaP
Ships

## Slide 6
BiOMaP radiometric data form various European Seas
G. Zibordi, J.-F. Berthon, F. Mélin and D. D’Alimonte. Cross-site consistent in situ measurements for satellite ocean color applications: the BiOMaP radiometric dataset. Remote Sensing of Environment,115, 2104–2115, 2011.

## Slide 7
Tri-Dimensional Mapping of BiOMaP radiometric data
G. Zibordi, J.-F. Berthon, F. Mélin and D. D’Alimonte. Cross-site consistent in situ measurements for satellite ocean color applications: the BiOMaP radiometric dataset. Remote Sensing of Environment,115, 2104–2115, 2011.

## Slide 8
Tri-Dimensional Mapping of BiOMaP radiometric data
G. Zibordi, J.-F. Berthon, F. Mélin and D. D’Alimonte. Cross-site consistent in situ measurements for satellite ocean color applications: the BiOMaP radiometric dataset. Remote Sensing of Environment,115, 2104–2115, 2011.

## Slide 9
SeaWiFS –BiOMaP Match-Ups (including Black Sea)
G. Zibordi, J.-F. Berthon, F. Mélin and D. D’Alimonte. Cross-site consistent in situ measurements for satellite ocean color applications: the BiOMaP radiometric dataset. Remote Sensing of Environment,115, 2104–2115, 2011.

## Slide 10
MODIS –BiOMaP Match-Ups (including Black Sea)
G. Zibordi, J.-F. Berthon, F. Mélin and D. D’Alimonte. Cross-site consistent in situ measurements for satellite ocean color applications: the BiOMaP radiometric dataset. Remote Sensing of Environment,115, 2104–2115, 2011.

## Slide 11
Bio-optical models: the tools to convert satellite atmospherically corrected data into high-level products
Seawater Optically Significant Components (Phytoplankton biomass, Suspended & Dissolved Matter).
Satellite derived marine signal (“Reflectance” Rrs)
statistical
Chla~f(Rrs(l1),Rrs(l2))
semi-analytical
a,bb~(Rrs(l))
Chla~ (l, a, bb)

## Slide 12
D. D’Alimonte, G. Zibordi, J.-F. Berthon, E. Canuti and T. Kajiyama. Bio-optical Algorithms for European Seas: Performance and applicability of Neural-Net Inversion Schemes. JRC Scientific and Technical Report EUR 24920 EN (2011).
Schematic of MLP with two layers of adaptive parameters

## Slide 13
D. D’Alimonte, G. Zibordi, J.-F. Berthon, E. Canuti and T. Kajiyama. Bio-optical Algorithms for European Seas: Performance and applicability of Neural-Net Inversion Schemes. JRC Scientific and Technical Report EUR 24920 EN (2011).
Performance of the BiOMaP MLP NN for various ocean color products

## Slide 14
Expand current AOP Analysis including Data from the NATO Project;
Investigate AOP Features at Sub-Basin Level;
Investigate Commonalities in Bio-Optical Features between Black Sea and other EU Seas.
Future developments